STM32 Course
First Project – GPIO Ports
PRESENTED BY:
Johan Svensson

---
Content
- Components: Resistor, Capacitor, LED, Button
- General Purpose Input Output (GPIO) – Input, Output
- Reset and Clock Controller (RCC), Debug
- Electrical schematic: STM32, Resistor, LED, Button
- First project

---
Components: Resistor
- Measured in [Ohm]
- Many application, example:
- Voltage dividers
- Control the current
- Filters
- Source: wikipedia.org

---
Components: Capacitor
- Measured in [Farad]
- Applications:
- RC-filter
- Button bouncing
- Bypass capacitor
- Source: wikipedia.org

---
Components: LED
- Light Emitting Diode
- Anode (+)
- Cathode (-)
- Source: wikipedia.org

---
Components: Button (Switch)
- Used to open and close a path
- Button bouncing, see graph
- Hardware, add capacitor
- Software, add delay to suppress the transient

---
RCC
Sets the system and peripheral clocks

---
RCC
- High Speed Clock
- Low speed Clock
- Master clock output

---
Debug
- Debug: No debug, <serial wire>, JTAG (4 pins), JTAG (5pins), Trace as Asynchronous Sw
- HW breakpoints

---
GPIO – Input
- IRQ: get a notification when the input has changed state
- Polling: checking if the input has changed state

---
GPIO – Input
Pull-down(rising edge), Pull-up (falling edge)

---
GPIO – Input (IRQ)
- GPIO mode:
- External IRQ mode with rising edge, falling edge or both
- External Event mode with rising edge, falling edge or both
- GPIO pull-up/pull-down: No pull-up and no pull-down, pull-up, pull-down
- User label:

---
GPIO – Input
- GPIO mode: Input mode
- GPIO pull-up/pull-down: No pull-up and no pull-down, pull-up, pull-down
- User label:

---
GPIO – Output
- GPIO Output level: Low, high
- GPIO Mode: Output push, pull and Output open drain
- GPIO pull-up/pull-down: No pull-up and no pull-down, pull-up, pull-down
- Maximum output speed: Low, medium, high
- User label:

---
Electrical schematic

---
First project
- Read from one GPIO (Polling) and change state on one LED.
- Interrupt from one GPIO (IRQ), When the switch is closed the LED will change state.