Xubuntu Q
Project 1 - GPIO
STM32 Course

---
Content
- Components: LED, Resistor, Capacitor, Button
- RC Filter, Button Bouncing, Pull-up, Pull-Down Resistor
- General Purpose Input Output (GPIO)
- Reset and Clock Controller (RCC), Debug
- Electrical schematic
- First project

---
Components: LED
Light Emitting Diode

---
Components: Resistor
- Measured in [Ohm]
- Applications:
- RC Filters
- Voltage divider
- Control the current

---
Components: Capacitor
- Measured in [Farad]
- Applications:
- RC-filter
- Bypass Capacitor

---
Components: Button (Switch)
- Used to open and close a path
- Button bouncing

---
RC Filter

---
Button Bouncing
- Hardware
- Software

---
Pull-up, Pull-Down Resistor

---
RCC
Set the system and peripheral clocks

---
RCC
- High Speed Clock
- Low speed Clock
- Master clock output

---
Debug
- Debug: Serial Wire, JTAG (4 pins), JTAG (5pins), Trace as Asynchronous Sw
- HW breakpoints

---
GPIO – Input
- Interrupt: get a notification when the input has changed state
- Polling: check if the input has changed state

---
GPIO – Input (Interrupt)
- GPIO mode:
- External IRQ mode with rising edge, falling edge or both
- External Event mode with rising edge, falling edge or both
- GPIO pull-up/pull-down: Pull-up-, Pull-down- resistor, none
- User label

---
GPIO – Input
- GPIO mode: Input mode
- GPIO pull-up/pull-down: Pull-up-, Pull-down- resistor, None
- User label

---
GPIO – Output
- GPIO Output level: Low, High
- GPIO Mode: Output push, pull and Output open drain
- GPIO pull-up/pull-down: Pull-up-, Pull-down- resistor, none
- Maximum output speed: Low, Medium, High
- User label

---
Electrical schematic

---
First project
- Interrupt: Toggle state of LED
- Polling: Set button pin state to LED state