First Project
STM32 Course

---
Contents
- Components: Resistor, LED, Button
- GPIO – Input, Output
- STM32: Reset and Clock Controller (RCC), Debug
- Electrical schematic: STM32, Resistor, LED, Button
- Eclipse shortcuts
- First project

---
Components: Resistor
- Resistors are measured in [Ohm]
- Can be used for voltage dividers
- Used with LED to control the current
- Filters
- Source: wikipedia.org

---
Components: LED
- Light Emitting Diode
- Anode (+)
- Cathode (-)
- Source: wikipedia.org

---
Components: Button (Switch)
- Used for open and closing a path
- Button bouncing, see graph
- Hardware, add capacitor
- Software, add delay to suppress the transient

---
STM32: RCC
Sets the system and peripheral clocks

---
STM32: RCC
- HSE
- LSE
- Master clock output
- If we want to have a clock that acts as a master for other devices

---
STM32: Debug
- Debug: No debug, <serial wire>, JTAG (4 pins), JTAG (5pins), Trace as Asynchronous Sw
- System wake-up, assigns a GPIO for wake-up
- Timebase source: <Systick>, TIM1, TIM2, TIM3, TIM4 – Sets

---
GPIO – Input
- Polling: checking if the input has changed state
- IRQ: get a notification when the input has changed state

---
GPIO – Input (polling) stm32
- GPIO mode: Input mode, no pull-up and no pull-down
- GPIO pull-up/pull-down: No pull-up and no pull.-down, pull-up, pull-down
- User label: Choose a name for the pin

---
GPIO – Input (IRQ) stm32
- GPIO mode:
- External IRQ mode with rising edge, falling edge or both.
- External Event mode with rising edge, falling edge or both.
- GPIO pull-up/pull-down: No pull-up and no pull.-down, pull-up, pull-down
- User label: Choose a name for the pin

---
GPIO – Input (IRQ)
Rising or falling edge

---
Electrical schematic

---
Eclipse shortcuts
- ctrl+tab: go between header and source file
- ctrl+shit+r: open resource
- F3: open declaration
- ctrl+space: Show proposals, auto complete
- ctrl+shift+g: When a function, object or var is selected : find all occurences of it in the project.
- ...

---
First project
- Read from one GPIO (Polling) and change state on one LED. If switch is closed, LED is turned on. If switch is open, LED is turned off.
- Interrupt from one GPIO (IRQ), When the switch is closed the LED will change state. If the LED is turned on, it will be turned off and vice versa.